Band Saw Safety

- Operate only with instructor permission and after you have received proper training.

- Remove jewelry, eliminate loose clothing, and confine long hair.

- Always wear proper eye protection.

- Make sure all guards are in place and operating correctly.

- Make sure all adjustments are tight and secure.  Make sure that the blade is inside of the blade guard and that it is not loose.

- The upper blade guards should be place 1/8th of an inch above the work piece.

- Guide the work slowly; let the machine do the work.  Do not force the work into the blade.

- Do not attempt to cut a smaller radius than the blade will allow.

- Never back out of a cut while the machine is running.

- Place hands or fingers on each side of the cut line, never on the line.  Use a push stick if your fingers will come within 3-4 inches of the blade.

- Never leave the machine while it is still running.  Always wait for it to come to a complete stop.

- Use relief cuts when possible.