Scroll Saw Safety

- Operate only with instructor permission and after you have received proper training.

- Remove jewelry, eliminate loose clothing, and confine long hair.

- Make sure all guards are in place and operating correctly.

- Always wear proper eye protection.

- Make sure all adjustments are tight and secure and that the blade guards are properly adjusted.

- The blade should be held firmly in the chucks and be supported by the guide assembly.

- The teeth of the blade must always point down.

- Make sure that the hold down is pressing lightly on the work piece before cutting.

- Always place the flat side of the board against the table.

- Guide the material through the machine with both hands.  Your fingers should be at least 3-4 inches from the blade at all times and never in a direct line with it.

- To remove or change the blade, turn the large red knob on the top of the machine to loosen.  Push down on the upper chuck and remove the blade.  Replace the blade and tighten red knob.