Coping Saws

- Are used to cut curved shapes easily.

- The blade may be inserted in either direction.

- To remove or replace the blade, hold the pin closest to the handle and turn the handle counter clockwise.

- When cutting, be sure to use the entire length of the blade.

Drills

- When drilling, always place a piece of scrap lumber under your work piece to avoid splintering the wood.

- Be sure that the drill is spinning clockwise.

- Always check the electrical cord for any cuts or damage.

- Always remove the chuck key before turning on the drill.

- Allow the drill bit to cool off after each use.  Heat friction can make a drill bit hot enough to burn your skin.

Measuring Tools

- The try square and combination square are used to make 45 and 90 degree angles.

- Rules, scales, zig zags, and tape measures all use the inch scale.