Hand Saws

- When laying out your design, always remember to add the thickness of the blade (about 1/8th of an inch).

- Always cut on the waste side of the line.

- Secure the work piece in a clamp or a vise.

- Identify the grain of the wood and select the correct saw (below).

- Pull the saw back three times to start the cut.  Use your thumb as a guide, placing it well above the board to prevent injury.

- Support the piece being cut to prevent splintering when it falls.

Grain-dark brown lines

RIP SAWS

- Large teeth

- Used to cut in the same direction as the grain

- Hold the saw at a 60 degree angle

CROSSCUT SAWS

- Have small teeth

- Used to cut across the grain

- Hold the saw at a 45 degree angle