Drill Press Safety

- Operate only with instructor permission and after you have received proper training.

- Remove jewelry, eliminate loose clothing, and confine long hair.

- Make sure all guards are in place and operating correctly.

- Always wear proper eye protection.

- Hold materials securely with a clamp, a vise, or a jig.

- When possible, the long end of the material should be placed to the left of the machine.

- Always remove the key from the chuck.

- Select properly sharpened bits.

- Center punch metals and plastics before drilling.

- Turn off the power if a work piece is caught on the drill.  Do not try and stop it by hand!

- Adjust the depth stop to avoid drilling into the table or when a thru hole is not required.

- Select the correct speed for the material to be drilled.  Slow for metal or larger diameter drill bits.